## Slide 1: Course 5 – Electricity and Circuits

## Slide 2: Objectives
Circuit components
  Cells/batteries
  Loads
  Resistors
  Switches
  Wires
  Overcurrent
  Protection devices

## Slide 3: Relevancy
To understand the basics of electricity
To promote an engineering mindset
NABCEP PV Associate certification
CVQ level 2

## Slide 4: Cells
An electrochemical device consisting of two electrodes made of different materials and an electrolyte
Voltage is produced when a chemical reaction occurs between the electrodes and electrolyte

## Slide 5: Battery
Consists of two or more cells electrically connected together and packaged as a single unit
Often used to refer to multi-cell or single cell

## Slide 6: Types of Cells
Lead-acid
Nickel-cadmium (NiCd)
Carbon-zinc
Alkaline-manganese dioxide
Lithium

## Slide 7: Cells and Batteries
Normally classified as primary or secondary
  Primary types have a non-reversible reaction
  Secondary types have a reversible reaction (rechargeable)
Also classified as dry and wet cell
  Dry cells contain either a paste or gel electrolyte
  Wet cells must be used upright
All batteries have an internal resistance

## Slide 8: Primary vs Secondary
Primary cells are single use
  Alkaline
  Carbon-zinc
Rechargeable cells can be recharged
  Lithium-ion
  Lead-acid
  Nickel-cadmium

## Slide 9: Dry vs Wet Cells

## Slide 10: Cell Comparison
These are some of the cells that you may come across in photovoltaics
(Sailors for the Sea, 2016)
Notes: Batteries-01_0.png (560×310) (sailorsforthesea.org)
(Sailors for the Sea, 2016)

## Slide 11: Ratings
Capacity of a cell/battery is rated in ampere-hours (Ah)
Capacity can change based on:
  Temperature
  Current drain
  Discharge schedule
  Final output voltage
With a specified voltage, watt-hours can be calculated

## Slide 12: Lighting Loads
Incandescent
CFL
Miniature lamps
LEDs
Neon
Fluorescent

## Slide 13: Types of Resistors
Carbon-composition
Wire-wound
Cermet
Deposited-film
Conductive-plastic
Surface-mount

## Slide 14: Switches
SPST – single pole single throw
SPDT – single pole double throw
DPST – double pole single throw
DPDT – double pole double throw
Rotary

## Slide 15: Wires and Cables
Solid
Stranded
Romex
Metallic
TC
Wire gauge

## Slide 16: Overcurrent

## Slide 17: Protection Devices
Fuses
Circuit breakers
Fuse resistor
Voltage sensitive/voltage dependent resistor