## Slide 1
Design and Implementation of Pilot of a TVET Renewable Energy Course
DELIVERABLE #5 - TRAINING COURSES & PROFESSIONAL DEVELOPMENT
Session 31 (07 October 2022) – C09 Electricity and Circuits 2

## Slide 2: Topics
Understand the battery as a source of electricity.
Understand series and parallel connections for batteries.
Describe the different types of batteries used in RE systems.
Understand magnetism, motors and generators.
Understand how the electric grid operates related to small RE systems

## Slide 3: 2. Term 2 Course Introductions
C 09: Electricity and Circuits 2
Elec. Cir. 2 (in Calendar Table)
Introduce the battery as a resource of stored electricity
Series & parallel connections for batteries & PV panels
List the types of batteries
Understand magnetism, motors and generators
Introduce alternating current (AC), voltage, and power
Understand types of wire and cable

## Slide 4: 2. Term 2 Course Introductions
C 09: Electricity and Circuits 2
Examples of anticipated outcomes after course completion
Review & identify, existing & potential, wire & cable sizes
Review & identify from drawings and at a customer’s house, the battery type(s) with connections to PV panels
Demonstrate understanding of how direct current from a PV panel source can become alternate current in a home Plan and use portable generators at customer’s home

## Slide 5: 2. Term 2 Course Introductions
C 09: Electricity and Circuits 2
Instructor Comments?
Instructor Discussion?
Instructor Suggestions?
“Real World” Applications?

## Slide 6: Relevancy
Understanding the impact of electrical
To promote an engineering mindset

## Slide 7: Why Batteries?

## Slide 8: Terminology
Cycle – a complete discharge and recharge of the battery
Cycle life – the quantity of cycles the battery can endure
Capacity – amount of energy stored measured in Watt-hours
Specific gravity – ratio of density to a reference material

## Slide 9: Terminology
Self-discharge - how much the battery discharges without load
Gassing – when charging is faster than absorption, which produces heat
Thermal runaway – When a battery charges too fast and generates excess heat
Sulfation – excess buildup of lead sulfate to plates
Equalization – A process to decrease sulfation on plates

## Slide 10: Terminology
Peak load – the power required to start the load
Average load – the power it takes to keep a load running
Duty Cycle – also called depth of discharge
Inverter – converts DC to AC

## Slide 11: What is a Battery?
An electrochemical energy storage
Converts chemical energy to electrical energy
Has a positive and negative terminal

## Slide 12: Parts of a battery
This Photo by Unknown Author is licensed under CC BY

## Slide 13: Types of Batteries
Lead acid
  Flooded
  Sealed
Lithium
  Lithium-ion
  Lithium-Iron-Phosphate

## Slide 14: Flooded Lead Acid
Wet cell
Cheap
Requires ventilation
Low depth of discharge (DoD) @ 50%
Upright storage
Low cycle life
Requires regular maintenance

## Slide 15: Absorbent Glass Mat (AGM)
More expensive the lead acid
Cheaper than lithium
Capable of 80% DOD
Maintenance free
Low cycle life

## Slide 16: Lithium-Ion
Requires little maintenance
Expensive
Higher energy density (150-200 Wh/kg
High depth of discharge
Little thermal protection

## Slide 17: Lithium Iron Phosphate (LiFePO4)
Requires little maintenance
Expensive
High energy density (90-120 Wh/kg)
High depth of discharge
Safer from thermal runaway

## Slide 18: Thermal Runaway

## Slide 19: Questions?

## Slide 20: Connections
Series
Parallel
Series-parallel

## Slide 21: Rooftop Trainer
PV 1: 60 cell
250 – 350 W
PV 2
PV 3
PV 4
PV 5
PV 6
μ inverter
μ inverter
μ inverter
Terminator
AC Disconnect
240 VAC
< 10 amp
To Lab High Voltage Trainer
Trenched conduit
μ inverter
μ inverter
μ inverter

## Slide 22: Rooftop Trainer
PV 1: 60 cell
250 – 350 W
PV 2
PV 3
PV 4
PV 5
PV 6
DC Disconnect/
Combiner
150 DC
Circuit Breakers
To Lab High Voltage Trainer
Trenched conduit

## Slide 23: Magnets

## Slide 24
·
X
Voltage is induced when conductors cut lines of flux.
Green arrow shows direction of conductor movement.
Dot and X show direction of current caused by voltage.
No voltage is induced when conductors move parallel
to the to the lines of flux.
Induced Voltage

## Slide 25: Sine Wave Generation

## Slide 26: Sine Wave

## Slide 27: Voltage Generation

## Slide 28: Questions?

## Slide 29: Power Generation
A hydroelectric turbine converts the kinetic energy to electricity

## Slide 30: Power Generation

## Slide 31: Power Generation

## Slide 32: Power Generation

## Slide 33
Phase 3
Phase 2
Phase 1
Line 1
Line 2
Line 3
Delta-Connected Source
The sum of the instantaneous
phase voltages equals zero.
Delta-Connected Load
Each load resistor will be
connected to one of the phases.
For the delta-to-delta connection, Vline = Vphase = Vload.
For the delta-to-delta connection, Iline = 1.732 Iphase = 1.732 Iload.
Delta Connections

## Slide 34
Line 3
Line 2
Line 1
Wye-Connected Source
Wye-Connected Load
I line = Iphase = Iload.
Vline = 1.732 Vphase = 1.732 Vload.
For the wye-to-wye connection with a balanced load:
Phase 3
Phase 1
Phase 2
There is no voltage between the source and load star-points.
Wye Connections

## Slide 35: Electric Motor
Like a generator
Uses electricity to provide drive load

## Slide 36: Questions?